## Slide 1: Design and Implementation of KY Buck-Boost Converter with Voltage Mode Control
A Voltage Mode Control Approach for DC-DC Converters
Shivam Saini
IIT Ropar

## Slide 2: Introduction
• KY Buck-Boost Converter provides stable voltage output for variable input sources.
• Combines a KY Boost and Synchronous Buck converter.
• Applications: Portable devices, renewable energy systems, EV charging.

## Slide 3: Design of KY Buck-Boost Converter
• Circuit Design Overview
• Key Components:
- Switches: S1, S2
- Inductors: L1, L2
- Capacitors: C1, C2, Co
• Specifications:
- Input Voltage: 10V-16V
- Output Voltage: 12V
- Load Current: 2A
- Switching Frequency: 10kHz

## Slide 4: Working Principle
• Mode I (S1 ON, S2 OFF):
- C1 charges, L1 magnetizes.
- C2 discharges, L2 magnetizes.
• Mode II (S1 OFF, S2 ON):
- L1 demagnetizes, C2 charges.
- Energy transfer to output.

## Slide 5: Voltage Conversion
• Voltage conversion ratio: Vo/Vin = D/(1-D)
• Buck Mode: Output Voltage < Input Voltage (D < 0.5)
• Boost Mode: Output Voltage > Input Voltage (D > 0.5)

## Slide 6: Simulation Results
• MATLAB Simulation Output:
- Buck Mode: 16V input, 12V output.
- Boost Mode: 11V input, 12V output.
• Stable output voltage achieved.

## Slide 7: Experimental Results
• Buck Mode: 16V input, 12V output.
• Boost Mode: 11V input, 12V output.
• Dynamic response for step input changes.

## Slide 8: Conclusion
• KY Buck-Boost converter provides a simple and efficient solution for variable input voltages.
• Ensures system stability and fast transient response.
• Suitable for low-power portable applications.